## Slide 1: BCC AV Digital Upgrade
October 2018

## Slide 2: why do we need an upgrade ?
Date of manufacture 2007 - AV control
Install contract is dated March 19, 2008
Failing Equipment , Company no longer manufacturing any of the analog models we have installed, equipment has no service warrantee.
Poor forethought to AV design principals (underpowered Amplification, low lumen projectors in bright areas, loud operation of equipment)

## Slide 3: Cost for equipment only
 | Cost |  | Equipment /Tools/Software/Hardware
For already equipped classrooms | $2,468 | Upgrade of audio visual control systems Projection | MCL plus 100 +1604 +DTP 230rx Extron MLC Plus 100 interfaces Extron In 1604 switcher/ scaler/ transmission Extron DTP HDMI 4K 230 Rx receiver
 | $5000 |  | Panasonic PT-RZ570WU laser projector
Total | $7,468 |  | Labor, programming and cabling not included.

## Slide 4: Advantage of digital Upgrade
Brighter ,more visible teaching materials. Using presentation Technology to engage students is effective.
Every year the projectors have 600 hours on average put on them. We need to change on average of 12 sets of bulbs per year at $400 per bulb, and change filters regularly. with up grade laser projectors work for 7 years with no bulb replacements
Showing High definition for PowerPoint , Keynote and all presentations is the industry standard.
Some programs will not show complete interface with standard definition projectors

## Slide 5: Rooms that need Upgrade
list of room to be addressed to support HD video and Future Proof Room.
Auditorium
14, 15, 31,32,33,34
,51,52,53,54,55,57,126
213,223,226,227, 313,312,323

## Slide 6: rooms that need projector Only upgrade
Current Backbone is sufficient for HD signal.
421.422 ,423,424
411,413,431
513,514,518,521,522

## Slide 7: Scheduling upgrade has to start - we have a lot of Deferred maintenance
20 rooms need Full upgrade. Equipment and cabling.
11 rooms need Projector and programming to be upgraded.
we need to start doing at least 5 rooms per year to get upgraded in 6 years.

## Slide 8: How Are we going to pay for this?
Aquire bids once we decide on design.
CTE funds?
Grants?
Bonds?
Donations?